## Slide 1: Soil quality indictors in Life Cycle Assessment
CSIRO Sustainable Agriculture Flagship
Sandra Eady and Tim Grant
8 and 9 April 2014

## Slide 2: Setting the scene
What is an LCA
Why undertake LCAs
Life cycle inventory activities to date in Australia

## Slide 3: What is a Life Cycle Assessment?
LCA is the most commonly used tool to determine the environmental impact that a product or service has, by taking into account all of the impacts from resource extraction, production, use, through to end of life disposal.
Source: Ryan, S 2012. Buying Choices for a More Sustainable Canberra, Report for the ACT Commissioner for Sustainability and the Environment

## Slide 4: Interaction between the economy and environment
4
Economy /
Technosphere
Realm of human
activity
“Flows” associated with soil degradation
Source: RMIT LCA Course Notes

## Slide 5
Life cycle inventory of environmental flows – CO2 NOx Pb, land ect
Climate
Ozone layer
Acidification
Smog
Carcinogen
Fossil fuel
Ecotoxicity
Nutriphication
Minerals
Land-use
Radiation
Seawater
level
Dying
forests
cancer
Extinction
of species
Respiratory
diseases
Reduced
resource
base
Human Health
Ecosystem Health
Social
Equity
Environmental flows
Mid-point indicators (links in the cause-effect chain)
End points
Source: RMIT LCA Course Notes

## Slide 7: Reasons for environmental assessment (Life Cycle Assessment)
Environmental product declarations to inform consumer choice
  European Commission to adopt LCA as the approach to be used for environmental assessment of products for the ‘Single Market for Green Products’ (see http://ec.europa.eu/environment/eussd/smgp/product_footprint.htm).
Delivery agreements where the supplier is required to demonstrate an on-going improvement program of environmental sustainability
    EU, Japanese, Australian markets – especially supermarkets
The likely advent of trade agreements premised on climate change mitigation efforts
      Covered economies versus uncovered economies for carbon pricing

## Slide 8: Reasons for environmental assessment (Life Cycle Assessment)
Unilateral need to respond to global warming – triggered by realignment of insurance risk and costs to the economy
        Covered economies versus uncovered economies for carbon pricing
Negotiations for international agreements on greenhouse gas emissions reduction targets
      Especially China and India for export production (carbon footprint of exports)
Need to produce more food globally with a lower environmental impact
        Global significance but more so for countries that produce large amounts of staple foods – e.g. Australia, China, India, Africa, south America, north America, Russia……
Need to have a consistent framework for assessing the environmental impact of different industry sectors and combined impact in different regions
        Regional and national significance for evaluation of NRM investments, industry investment in sustainable production, ......

## Slide 9: Role of Life Cycle Inventory
Life Cycle Assessment is only as good as the underlying data or Life Cycle Inventory (LCI) that is used for the analysis.
Country specific LCI for agricultural products is essential for Australian agriculture to undertake environmental impact studies.
In the absence of country specific data, LCA practioners will use the next best data available and this is often from Europe and the USA (with ecoinvent® being the most used LCI).

## Slide 10: Advantages of a Public Inventory
Act as a repository for LCI from the many LCA studies being undertaken, to reduce duplication of common inventory e.g. wheat
Consistent approach applied to inventory across sectors e.g. consistent modelling of pesticide flows
Guidelines and standards can be set for:
  Transparency
  Data quality
  Review
  Standard formats
Inventory can be structured so that it can be efficiently updated e.g. change in N2O emissions factor for N fertiliser use, improved flows model as GIS data is updated nationally.

## Slide 11: LCI Activities in Australia
Series of guideline documents on data collection, reviewing, best practice guide now available on AusLCI website
Major project by BPIC now completed with gate-to-gate data published, needs further development to be integrated into full life cycle unit process LCI.
AusAgLCI – commenced in Dec 2011, will cover major products, public research agency providing data, funding support from industry, goal is unit processes from cradle-to-farm gate.
Extensions to AusAgLCI – Department of Agriculture Innovation Fund project for grazing and general cropping inventory (CSIRO and LCS; March 2014) and GRDC project for detailed cropping systems including rotations (NSW DPI, CSIRO and LCS; July 2014)

## Slide 12: Over to Tim........
Elementary flow, cause and effect pathways, impact assessment in general
Approaches taken for different land-based impact categories
How should we think about soil indicators in the context of LCA

## Slide 14: Elementary flow
material or energy entering the system being studied that has been drawn from the environment without previous human transformation, or material or energy leaving the system being studied that is released into the environment without subsequent human transformation
Source ISO 14044

## Slide 15: Examples of elementary flows
Mineral ores
  Lead ore, in ground
  Lead, 5.0% in sulfide, Pb 3.0%, Zn, Ag, Cd, In, in ground
  Lead, Pb 0.014%, Au 9.7E-4%, Ag 9.7E-4%, Zn 0.63%, Cu 0.38%, in ore, in ground
Fuels
  Coal, brown in kg
  Coal, brown, 10.0 MJ per kg, in ground in kg
  Coal, brown, 14.1 MJ per kg, in ground in kg
  Energy from brown coal in MJ
Land occupation and transformation
  Occupation, arable, conventional tillage in m2.years
  Transformation, from arable, non-irrigated, extensive in m2

## Slide 16: Examples of elementary flows
Soil –Raw material input
  Carbon, in organic matter, in soil
  Clay and soil, extracted for use
  Clay and soil, related unused extraction
  Soil, unspecified, in ground
Emission to air
  Particulates
  Particulates Matter >10um
  Particulate Matter 10.0 um
  Particulate Matter 2.5 um

## Slide 17: Examples of elementary flows
Water emissions
  Soil loss by erosion into water
  Organic substances, unspecified
  Solved substances
  Solved substances, inorganic
  Suspended substances, unspecified
  Salts, unspecified
  Acidity, unspecified
Soil emissions
  Salts, unspecified
  Acidity, unspecified

## Slide 18: Examples of elementary flows
Biomass

## Slide 19: How many elementary flows are there
In SimaPro
  Raw materials 1800
  Air emissions 4700
  Water emissions 3700
  Soil emissions 3400
  Also emission sub-compartments for air water and soil emissions
Air | Water |  | Soil
non-urban air or from high stacks | ground- |  | agricultural
low population density, long-term | ground-, long-term |  | forestry
lower stratosphere + upper troposphere | ocean |  | industrial
urban air close to ground | surface water |  | unspecified
indoor | unspecified |  | 
unspecified |  |  | 

## Slide 20: How to position the elementary flow.
Elementary flow definitions should enable meaningful aggregation in the impact assessment model.
Timber production
  Flow of standing hardwood, in mass units, - or
  Land occupation in area time and land transformation in area?
  Which is better to aggregate and predict effects on biodiversity?

## Slide 21: Adding up the trees
= ?

## Slide 22: Area of land use change
= ?

## Slide 23: New types of elementary flows
Social Hot Spot database – risk levels used for attributes
Risk of Child Labor in sector, Female , VHR
Risk of Child Labor in sector, Female , HR
Risk of Child Labor in sector, Female , MR
Risk of Child Labor in sector, Female , LR
Risk of Child Labor in sector, Female , URL
Risk of Child Labor in sector, Female = ne

## Slide 24: New types of elementary flows
Water footprint flows – adding geography to elementary flows
Water, lake, AE
Water, lake, AF
Water, lake, AL
Water, lake, AM
Water, lake, AO
Water, lake, AR
Water, lake, AT
Water, lake, AU
Water, lake, AZ
Water, lake, BA
Water, lake, BD
Water, lake, BE
Water, lake, BF

## Slide 25
The environmental mechanism – example of human toxicity
Emissions in compartment m
Time integrated concentration  in n
Dose taken in
Risk of affected persons
Damage on human health
Chemical fate
Human
exposure
Potency
(Dose - response)
Fraction transferred to n
Severity
Intake fraction iF
Effect factor
(ES&T 2002, 36, 207-212 A)

## Slide 26: Current approaches to land use
Biodiversity metrics based:
  Direct occupation of land – displacing biodiversity and stopping it re-establishing on that land
  Increased segregation of remaining natural land.
Japanese LIME model included NPP as an endpoint in LCA.
Ecological footprint- based on exclusive use of land based on NPP.
ILCD – carbon deficit from land use change.
World impact+ method – focus on regionalisation of impact assessment – included soil ecological functions – erosion resistance, water supply, water filtration.

## Slide 27
The scope of our work for the next two days
Source: Garrigues et al. 2013. Development of a soil compaction indicator in life cycle assessment. International J Life Cycle Assessment 18:1316.

## Slide 28: Back to Sandra
Current flows in AusAgLCI to cover impact categories
Inventory produced to date
Some LCI results
Expectations from the workshop

## Slide 29: Impact categories
Global warming:
  Flows are based on IPCC (2006) and National Inventory Report (DCCEE 2011) methodologies.
  Emissions directly associated with production (e.g. direct and indirect GHG emissions from fertiliser use, burning of stubble, crop residues) are included as inventory flows but not potential carbon sinks and sources (soil, litter and vegetation carbon changes); it will be the domain of the LCA practioner to add these where appropriate.
Water use:
  Elemental flows required to support a range of impact assessment approaches are included. Green water is included if there is a land transformation that changes the availability of water downstream for other users.
Land use:
  The land cover classifications used by ecoinvent® are used as the basic flow in the inventory.
  To inform the discussion on land use and the competing demands for land, an approach that classifies both area and the capacity of land to produce food is required.

## Slide 30: Impact categories - continued
Eutrophication:
  Nitrogen flows are estimated using Australian NIR methodology and phosphorus flows are estimated by the method used by ecoinvent®.
  Both methods are responsive to fertiliser inputs, and use regional data (at the intersection of GIS layers for agro ecological region and land use) to determine if leaching and run-off is occurring, and to estimate net export of soil (relevant for P transport to waterways).
Ecotoxicity:
  Flows of specific active ingredients to soil, water and air are estimated from PestLCI, adapted to Australian conditions.
  Parameters modified for Australian conditions are climate related (temperature, precipitation, evaporation, solar radiation), soil characteristics (depth, proportion sand, silt and clay, pH, organic content, bulk density), and field data (slope).
  Profiles for use in PestLCI have been constructed from GIS layers at the intersection of agricultural land use and agro ecological region.
  A number of pesticides used in Australia have been added to the model, using readily available data on key parameters (molecular weight, solubility, vapour pressure, half life in soil).
Notes: The methods do not take into account more detailed spatial and temporal variation in weather and soil conditions. Approaches to quickly locate relevant data on nutrient flows at this finer scale were investigated, in the first instance using BiosEquil (Raupach et al. 2001). The work required to successfully complete this was beyond the scope of the project but would be a sensible future investment.

## Slide 31: What has been produced to date
Sector | Processing | Material | Total
Cotton | 14 | 4 | 18
Horticulture | 17 | 16 | 33
Livestock* | 2 | 12 | 14
Grains | 19 | 16 | 35
Sugar | 13 | 7 | 20
Irrigation |  |  | 23
Other |  |  | 4
Total |  |  | 147
* Supporting inventory

## Slide 34: Preliminary Wheat GHG Results

## Slide 35
The scope of our work for the next two days
Day 1
Day 2
Source: Garrigues et al. 2013. Development of a soil compaction indicator in life cycle assessment. International J Life Cycle Assessment 18:1316.

## Slide 36
Sustainable Agriculture
  Sandra Eady Project leader
    t +61 2 6776 1394
    e sandra.seady@csiro.au
    w www.csiro.au
Life Cycle Strategies
  Tim Grant Project Partner
    t +61 3 8669 2048
    e tim@lifecycle.com.au
    w www.lifecycles.com.au
CSIRO Sustainable agriculture flagship